## Slide 1
Instructor: Mam Zulikha Kiran
Namal University, Mianwali
1
Electronic Devices and Circuit
BOOST CONVERTER USING MOSFET
Presenter:
Ahtisham Saleem
(NIM-BSEE-2021-19)

## Slide 2
2
Introduction
Circuit Diagram
Working of boost converter
Simulation Results
Calculations
References
Table of Content

## Slide 3
3
The Boost Converter is the Electronic device that uses a MOSFET (IRFZ44N MOSFET in my case) to convert its Low input DC Power into High output DC power.
The Boost Converter is a switched-mode power supply and this consist of at least two semi-conductor device and minimum one energy storage element.
In many domestic and industrial applications, there is a requirement for conversion of DC voltage source to different levels. Thus there is a need for a dc-to-dc converter that converts a fixed-voltage dc source into a variable-voltage dc source.
Introduction

## Slide 4
4
Circuit Diagram

## Slide 5
5
Boosting Mechanism: The boost converter increases the input voltage by utilizing the inductor's energy storage and release. When the switch is ON, the inductor stores energy. When the switch is OFF, this stored energy is released, boosting the output voltage.
Operation:
Switch ON: Inductor stores energy, charging the capacitor.
Switch OFF: Inductor releases energy, boosting output voltage and recharging the capacitor.
Working of boost circuit

## Slide 6
6
1. Duty Cycle:
Formula: Vout = Vin / (1 - D)
Calculation: 1 - D = 12V / 48V
Result: D = 0.75 (75%)
2. Inductor Value (L1):
Formula: L1 >= (Vin * D) / (2 * fsw * ΔIL)
Calculation: L1 >= (12V * 0.75) / (2 * 50kHz * 0.2A)
Result: L1 >= 225 μH
Working of boost circuit
3. Capacitor Value (C1):
Formula: C1 >= (Iout * D) / (2 * fsw * ΔVout)
Calculation:
  Iout = Vout / Rload = 48V / 100Ω = 0.48A
  C1 >= (0.48A * 0.75) / (2 * 50kHz * 0.1V)
Result: C1 >= 36 μF

## Slide 7
7
7
References
[1] https://electronicsmind.com/boost-converter/#google_vignette
[2]https://www.theengineeringprojects.com/2021/03/boost-converter-using-mosfet-irfz44n-in-proteus.html
[3] https://www.youtube.com/watch?v=Xqhvv3IPehE

## Slide 8
Thank You
Any Questions?
8